## Slide 1
EMBEDDED SYSTEMS CASE STUDY
23CSE304 | EMBEDDED SYSTEMS
Vehicle Event Logging and Response System
Register-Level Sensor Interfacing • Peripheral Configuration • Real-Time Event Handling on STM32F411CEU6
01 SENSOR ACQUISITION
M
MPU6050
I²C • Acceleration + angular rate
T
LM35* temperature sensor
ADC • Analog temperature input
D
HC-SR04* ultrasonic sensor
GPIO + TIMx • Echo pulse / distance
signals
STM32F411CEU6
ARM Cortex-M4 controller
Acquire • Process • Decide
I²C
ADC
TIMx
event data
02 EVENT CLASSIFICATION & RESPONSE
Evaluate thresholds
Filter readings; classify motion, heat or proximity
Update event state
Set event flags and apply alert priority in firmware
♪
Alert
Alert emergency services; via UART
SENSE → ACQUIRE → CLASSIFY EVENT → UPDATE STATUS → ALERT
PROJECT TEAM
01
Aniruth Karthik
CB.SC.U4CSE24502
02
Jaikkrish S
CB.SC.U4CSE24513
03
Krishanth K
CB.SC.U4CSE24521
04
Srisanth P A
CB.SC.U4CSE24550
EMBEDDED SYSTEM CONCEPTS
GPIO
I²C
ADC
TIMERS
EXTI / NVIC
SysTick
UART / USART
Register-level I/O
23CSE304 • 01 / 09

## Slide 2
23CSE304 | EMBEDDED SYSTEMS
Project Objectives, Boundaries & Validation
Vehicle Event Logging and Response System • Define the work, its limits, and how success will be verified
PROJECT OBJECTIVES
01
Acquire sensor measurements
MPU6050 via I²C • LM35* via ADC • Ultrasonic* via GPIO + TIMx
02
Interpret readings in firmware
Validate/filter data; compare configurable thresholds; classify motion, heat, or proximity events.
03
Respond with local alerts
Transmit emergency alerts through UART; define and test normal, warning, and critical states.
04
Verify system behaviour
Test each sensor separately, then verify the complete sensor-to-alert path under controlled conditions.
SCOPE BOUNDARIES
INCLUDED
Sensor acquisition
Threshold/event logic
GPIO LEDs + buzzer
Controlled validation
FUTURE PLANS
Verified collision ID
Faster alerts
Permanent event logs
Wireless notifications
SUCCESS CRITERIA | EVIDENCE TO COLLECT
MOTION
Observe a configured motion anomaly during a controlled movement test.
TEMPERATURE
Compare reading with a reference; alert above the set threshold.
DISTANCE
Check known distances; warn below the configured proximity threshold.
OUTPUTS
Verify the expected UART communication behaviour
INTEGRATION
Demonstrate all sensor paths driving the shared event logic and alerts.
Design principle: Monitor → Interpret → Respond | Validate with controlled tests; report measured results only.
23CSE304 • EMBEDDED SYSTEMS • VEHICLE EVENT LOGGING AND RESPONSE SYSTEM
02 / 09

## Slide 3
02 / ARCHITECTURE
System architecture & component dependencies
Each input uses a distinct interface; all measurements converge in the STM32 event-processing logic.
MOTION / ROTATION
MPU6050 IMU
Interface: I²C1
3-axis acceleration + 3-axis angular velocity
Purpose: motion anomaly / possible-impact detection
TEMPERATURE
Temperature sensor*
Interface: ADC1
Analog voltage → temperature estimate
Purpose: temperature-threshold monitoring
OBSTACLE DISTANCE
Ultrasonic sensor*
Interface: GPIO + TIMx
Trigger pulse → Echo duration → distance
Purpose: obstacle-proximity warning
STM32F411CEU6 | ACQUIRE • VALIDATE • DECIDE • RESPOND
1 ACQUIRE
I²C reads • ADC conversion GPIO input • timer capture
2 VALIDATE
Range checks • filtering Timeout / invalid-data handling
3 DECIDE
Threshold comparison Event classification • alert state
4 RESPOND
Alert via UART
TIMING & INTERRUPTS
SysTick: periodic scheduling | TIMx: Echo timing | EXTI/NVIC: optional interrupts
SENSOR ACQUISITION → VALIDATED MEASUREMENT → EVENT CLASSIFICATION → LOCAL WARNING
23CSE304 · EMBEDDED SYSTEMS | VEHICLE EVENT LOGGING AND RESPONSE SYSTEM
03 / 09

## Slide 4
03 / CONTROLLER IMPLEMENTATION
04
STM32F411CEU6: the role of the microcontroller
The MCU initializes peripherals, acquires sensor data, runs event logic, and controls warning outputs.
MICROCONTROLLER
STM32
F411CEU6
ARM Cortex-M4 + FPU
512 KB
Flash
128 KB
SRAM
12-bit
ADC
GPIO / I²C
TIM / USART
Peripheral setup + event logic
FEATURE → STM32 PERIPHERAL
MPU6050
I²C1; GPIO alternate-function setup
LM35*
ADC1; analog input configuration
HC-SR04*
GPIO trigger + timer input capture
Buzzer / LEDs
GPIO output; timer optional for patterns
Periodic tasks
SysTick or a general-purpose timer
Hardware events
EXTI + NVIC, if interrupt-driven
PC debug stream
USART asynchronous mode, if available
REGISTER CONCEPTS USED
RCC_AHB1ENR
Enable the GPIO peripheral clock
GPIOx_MODER / BSRR
Configure pins and drive outputs
I2C_CR1 / SR / DR
Control I²C and transfer data
ADC_CR2 / SQRx / DR
Configure conversion and read result
TIMx_PSC / CNT / CCRx
Set timer timing and capture
SysTick / EXTI / NVIC
Periodic scheduling / optional IRQs
STM32 registers configure the MCU; MPU6050 registers configure the external sensor over I²C.
STM32F411CEU6 · VEHICLE SAFETY MONITORING PROTOTYPE
04 / 09
Notes: This slide focuses on the STM32F411CEU6 controller role, the hardware-to-peripheral mapping, and the register groups used to configure those interfaces. Verify the exact temperature sensor marking before treating LM35 as confirmed. The MPU6050 has its own internal registers, configured over I²C; those are distinct from STM32 peripheral registers.

## Slide 5
04 / SENSOR INTERFACE
MPU6050 | Motion sensing and event classification
Six-axis IMU • I²C data acquisition • calibrated motion features • threshold-based event flags
01 / SENSOR OUTPUT
IMU
Accelerometer
X / Y / Z linear acceleration
Gyroscope
X / Y / Z angular velocity
SELECTABLE FULL-SCALE RANGES
Accel: ±2 / ±4 / ±8 / ±16 g
Raw data → physical units
At ±2 g: 16,384 LSB/g At ±4 g: 8,192 LSB/g Scale using the configured range.
Motion anomaly ≠ confirmed collision
02 / STM32 I²C INTERFACE
MPU6050
I²C slave
STM32F411
I²C master
SDA + SCL • 7-bit address 0x68 (AD0 low) or 0x69 (AD0 high)
KEY SENSOR REGISTERS
REGISTER
ADDR
PURPOSE
PWR_MGMT_1
0x6B
Wake sensor
SMPLRT_DIV
0x19
Sample-rate divider
CONFIG
0x1A
Digital low-pass filter
ACCEL_CONFIG
0x1C
Accelerometer range
ACCEL_XOUT_H
0x3B
Start of accel output
Read sequence
Register address → repeated START/read → 6 bytes → combine signed high/low words.
03 / FIRMWARE PROCESSING
1
Initialize I²C; wake and configure IMU
2
Read raw accel / gyro output registers
3
Combine bytes as signed 16-bit values
4
Scale, establish baseline, filter noise
5
Compare feature to configured threshold
OUTPUT EVENT FLAG
Main loop updates LEDs + buzzer
Optional: data-ready interrupt → EXTI/NVIC
VERIFY & TEST
Check breakout voltage/pull-ups • confirm pin + AF mapping and APB1 timing • calibrate stationary baseline • test repeatable motion cases
23CSE304 · EMBEDDED SYSTEMS | VEHICLE EVENT LOGGING AND RESPONSE SYSTEM
05 / 09

## Slide 6
05 / SENSOR 2
06
Temperature path: LM35 + STM32 ADC
The LM35 monitors temperature by producing an analog voltage that the STM32F411CEU6 digitizes using ADC1, converts into a temperature reading, and compares against a configured threshold to trigger a warning when exceeded.
SENSOR & WIRING
LM35
+VS
VOUT
GND
Analog temperature sensor
NOMINAL TRANSFER
10 mV / °C
VOUT → PA0 / ADC1_IN0 (example) GND → common STM32 ground
Keep ADC input within its allowed range (≤ VDDA). Check sensor supply and output range.
ADC CONVERSION & TEMPERATURE ESTIMATE
LM35 VOUT
ADC1 count
Temperature °C
STEP 1 • ADC COUNT → INPUT VOLTAGE
V_IN = (ADC_count / 4095) × V_REF
12-bit ADC: output code ranges from 0 to 4095.
STEP 2 • VOLTAGE → TEMPERATURE
T (°C) ≈ V_IN / 0.010
LM35 nominal scale factor: 10 mV per °C.
Then compare T against the configured threshold and set the event state.
Use the actual ADC reference voltage. A nominal 3.3 V is valid only when confirmed for the board.
STM32F411 ADC SETUP
1 RCC_APB2ENR
Set ADC1EN to enable the ADC1 clock.
2 GPIOA_MODER
Set the selected pin to analog mode.
3 ADC_CR1
RES bits select 12-bit resolution (00).
4 ADC_SMPR2
Set the sample time for ADC channel 0.
5 ADC_SQR3
Set SQ1 to channel 0 for the first conversion.
6 ADC_CR2
Set ADON; use SWSTART for software start.
7 ADC_SR / ADC_DR
Wait for EOC, then read the conversion result.
Resolution is not the same as accuracy.
STM32F411CEU6 · VEHICLE EVENT LOGGING AND RESPONSE SYSTEM
06 / 09

## Slide 7
06 / SENSOR 3
07
Ultrasonic ranging: HC-SR04 + STM32 timer capture
The HC-SR04 reports obstacle distance as an Echo pulse; the STM32 measures its high-time and converts it to range.
SENSOR & SIGNAL
HC-SR04
Non-contact obstacle ranging
TRIGGER → ULTRASOUND → ECHO
Echo high-time = t
Use a timeout if Echo never arrives; wait before the next measurement.
MEASUREMENT & DISTANCE CALCULATION
TRIGGER
WAIT ECHO
TIME HIGH
RANGE
DISTANCE FROM ROUND-TRIP ECHO TIME
d (cm) ≈ t_echo (µs) / 58
Approximation assumes sound speed near 343 m/s at room temperature.
TIMER CAPTURE SEQUENCE
1. Send a ≥10 µs Trigger pulse. 2. Capture Echo rising and falling edges. 3. Compute pulse width from timer counts and timer tick period.
TYPICAL MODULE VALUES
Nominal range 2–400 cm • 40 kHz ultrasound • 5 V supply (typical) • Allow >60 ms between measurements
STM32 INTERFACE & REGISTERS
EXAMPLE PIN MAP — VERIFY BOARD
VCC → 5 V | GND → common ground TRIG → PA8 GPIO output ECHO → PA9 / TIM1_CH2 via level shifter
RELEVANT TIMER REGISTERS
RCC_APB1ENR / APB2ENR
Enable the selected timer clock.
TIMx_PSC / ARR
Set timer tick and counter period.
TIMx_CCMR1 / CCER
Configure input capture and edge polarity.
TIMx_CCRx / SR
Read captured count; inspect capture flags.
ELECTRICAL SAFETY HC-SR04 Echo may output 5 V. Protect a 3.3 V STM32 input with a suitable divider or level shifter.
STM32F411CEU6 · VEHICLE EVENT LOGGING AND RESPONSE SYSTEM
07 / 09

## Slide 8
07 / FIRMWARE INTEGRATION
08
How the sensors work together
The STM32 turns sensor readings into validated event states; deployment software routes those events to the appropriate vehicle system.
01
INITIALIZE
Configure clocks, GPIO, I²C, ADC and timers
02
ACQUIRE
Read motion, temperature and obstacle distance
03
VALIDATE
Check range, sensor status and timeout conditions
04
CLASSIFY
Filter readings; compare with configured thresholds
05
ROUTE EVENT
Publish a typed event to the selected interface
EVENT CLASSIFICATION POLICY
Thresholds and event rules are firmware-configurable; exact values must be established during testing.
EVENT TYPE
CLASSIFICATION RULE
EVENT STATE / HANDOFF
MOTION
Filtered acceleration / rotation meets configured criterion
Set motion-event flag; attach measured values
TEMPERATURE
T ≥ configured T_threshold
Set temperature warning; include estimated temperature
PROXIMITY
Distance ≤ configured d_threshold
Set proximity warning; include estimated distance
DEPLOYMENT: VEHICLE-SYSTEM HANDOFF
The prototype validates event detection. In deployment, its local indicator output is replaced by an approved vehicle integration interface.
STM32 Event data
Approved integration
Vehicle / infotainment
The receiving system determines which supported response to perform. Android Auto or vehicle-network access requires platform-specific compatibility and authorization.
REAL-TIME CONTROL
SysTick / timer schedules periodic sampling • Timer input capture measures ultrasonic Echo • EXTI/NVIC is optional • Keep ISRs short and process events in the main loop
STM32F411CEU6 · VEHICLE EVENT LOGGING AND RESPONSE SYSTEM
08 / 09

## Slide 9
08 / VALIDATION
Validation plan & project conclusion
A planned test matrix defines the evidence and metrics needed to demonstrate reliable sensing and alert behavior.
VALIDATION MATRIX / PLANNED TESTS
TEST
METHOD
EXPECTED EVIDENCE
METRICS TO CAPTURE
MPU6050 motion
Stationary baseline; controlled movement
Repeatable accel. readings and event classification
Baseline variation; detection consistency; false triggers
Temperature
Compare at several conditions with reference thermometer
Temperature reading and threshold response
Reference vs. measured °C; absolute error (°C)
Obstacle distance
Measure known distances across repeated trials
Distance estimate and proximity alert
Reference vs. measured cm; absolute error (cm)
Alert response
Cross each configured threshold
Correct LED indication and buzzer behavior
Response time; correct / incorrect alerts
Fault handling
Simulate missing Echo or invalid sensor reading
Timeout; invalid data rejected; recovery behavior
Timeout duration; recovery outcome
Integrated operation
Exercise all sensor paths under controlled conditions
Consistent event decision; no conflicting outputs
Missed events; false alerts; response time
LIMITATIONS & ASSUMPTIONS
Verify sensor models, pinout and electrical compatibility.
Motion thresholds need calibration to reduce false detections.
Temperature and distance accuracy must be measured experimentally.
Invalid or missing readings must not produce misleading alerts.
Logging, wireless alerts and braking are outside current hardware scope.
PROJECT TAKEAWAY
The STM32F411CEU6 integrates motion, temperature and proximity sensing into a real-time, threshold-based warning prototype—demonstrating acquisition, event classification and local alert generation.
REPORTING RULE
This is a planned matrix. Enter measured results only after hardware testing.
NEXT: Verify hardware and pinout → Validate each sensor → Test events → Measure alert performance
23CSE304 · EMBEDDED SYSTEMS | VEHICLE EVENT LOGGING AND RESPONSE SYSTEM
09 / 09